# Video Processing
## Why?
With the internet becoming readily available to many more consumers, the range of networks and devices we are exposed to is increasing rapidly. To ensure that our content can be consumed by as many consumers as possible, it must be adapted and optimized to suit the needs of the consumer.
In order to do so, high-quality input videos must be processed to create multiple versions of the same file, each with a different resolution, bit rate and quality level, a process known as transcoding. Originally, video transcoding was employed in order to save storage space. However, as storage space is cheaper than ever, transcoding is now used to enable content streaming across platforms (our focus is on Adaptive HTTP Live Streaming).
## How?
To accomplish the entire video processing process in-house, the following technologies were used:
1. Ffmpeg: Cross-platform solution to convert audio and video from one format to the other. Ffmpeg also helps us in preparing the input video for Adaptive HTTP Live Streaming.
2. Ffprobe: Cross-platform solution to probe a media file for meta data like duration, video width/height, audio/video bit-rate, audio sampling rate, audio channels etc. This data helps in adding intelligence to our transcoder to decide the output file parameters.
3. JW Player: Video player that offers built in support for Adaptive HLS Streaming.

There are four major steps involved in the entire video processing process to prepare it for adaptive HTTP Live streaming with JW Player:
Probing media file for meta-data
Before actually transcoding the input media file, we must first decide the output media files' parameters, most importantly the video and audio bit-rates, the resolution, and the frame rate. In order to reach the optimum values for these parameters, we extract information from the input file using ffprobe.
Transcoding
Once we have all the meta-data from the input file, we perform various checks to evaluate the parameters for the output videos.
- Frame Rate
  We have set a base frame rate (currently 15 FPS) which we feel is optimum in most cases. The program selects the frame rate depending on which value is smaller, the base frame or the input video frame rate (doesn't make sense to upscale a video, since this increases file size needlessly without improving video quality).
- Video Bit-rate
  The process to calculate the video bit-rate is a bit more complex than the other calculations, since this factor alone dictates aspects such as the visual appeal and file size of the transcoded video.
  Based on the input file's aspect ratio, we first calculate the output file's width, given a certain vertical resolution (e.g. if the input file is a 16/9 video, and we want to scale it down to 360p, the output file will have a width of 360 * 16/9 = 640p). We do this to ensure that the scaling process doesn't stretch or shrink the video. By multiplying the width with the height, we get the number of pixels per frame; this value multiplied by the frame rate gives us the number of pixels per second. Since the bit-rate is defined in a unit like kilo-bits per second, we need to create an index, henceforth called pixel index, which defines the bits per pixel. We can multiply this with pixels per second to generate the bit-rate.
  The challenge lies in generating a pixel index matrix that can push down file size sufficiently, but not degrade video quality. Upon research, it was discovered that the bare minimum pixel index is 0.03 bits/pixel, which values above 0.1 have no noticeable effect. Keeping this in account, we generated the following matrix:
Resolution	Quality	Bits/Pixel
360p	LOW	0.040
	MEDIUM	0.062
	HIGH	0.089
432p	LOW	0.040
	MEDIUM	0.062
	HIGH	0.086
540p	LOW	0.040
	MEDIUM	0.063
	HIGH	0.083
720p	LOW	0.040
	MEDIUM	0.062
	HIGH	0.080
1080p	LOW	0.040
	MEDIUM	0.061
	HIGH	0.089

Using these values for the pixel index, we generated the optimum video bit rate. One last check is performed to see if this value is lower than the input video's bit-rate. If the input file's bit rate is already low enough (i.e. it is already a very low quality video), we do not use the calculated bit rate and instead proceed to lower other parameters of the input file.
Audio Bit-rate
Like the matrix for pixel indices, we also have a matrix for output audio bit-rate.
Resolution	Quality	Audio Bit rate (kbps)
360p	LOW	64
	MEDIUM	64
	HIGH	64
432p	LOW	64
	MEDIUM	64
	HIGH	64
540p	LOW	64
	MEDIUM	96
	HIGH	96
720p	LOW	128
	MEDIUM	128
	HIGH	128
1080p	LOW	256
	MEDIUM	256
	HIGH	256

The program simply looks into this matrix and pulls out the corresponding bit rate. This value is compared with the input file's audio bit-rate; if it is lower, we use this value in the transcoding process (doesn't make sense to upscale audio, since this increases file size needlessly without improving audio quality).

Resolution
Deciding the set of output resolutions is fairly simple. We have a set of defined resolutions (360p, 432p, 540p, 720p, 1080p) that we intend to support. The program simply converts the input video into all the resolutions below it. For example, an input video of 720p is converted into 540p, 432p and 320p. Additionally, if the input file has a pixel index higher than 0.1, a lower quality file of the same resolution is also created.
Once we have all the parameters of the output video, we simply need to invoke the ffmpeg command with the parameters we have calculated to transcode the file. Earlier, the program would invoke one ffmpeg process for each output resolution (3 processes if 360p, 432p and 540p outputs were to be generated). However, it was discovered that this was very CPU intensive and an overall slow process. To fix this, we used ffmpeg's built in support for generating multiple outputs from the same input file. Now, only one process is fired, regardless of the number of output resolutions.
Segmentation
To enable a video for HLS, it needs to be broken down into smaller segment files (.ts files), and all the segments need to be indexed via a play list file (.m3u8 files). Fortunately, ffmpeg has built in support for generating the segments and the play list file using the -stream_segment muxer (shorthand -ssegment) and -segment_list. This process is repeated for each output resolution. However, to enable Adaptive HLS, we need to provide JW Player with a combined .m3u8 play list that contains the information for the other play list files. This master.m3u8 is generated manually by the program since ffmpeg doesn't support this feature yet. This file can be supplied to JW Player to enable Adaptive HLS.
Earlier, the transcoding and segmentation processes were split, i.e. the system would first produce the transcoded mp4 files (1 ffmpeg process for multiple resolution outputs), and then further segment those files (1 ffmpeg process for each resolution file produced earlier). This was proving to be very time consuming, since the ffmpeg process had to go through the files twice. To streamline this process, the segmentation and transcoding was performed at the same time. Not only does this all work in one process, it was also much faster. These segments could later be concatenated (using -concat, built into ffmpeg) into one mp4 file if that file is needed for storage or fallback purposes (Note: the concatenation process is instantaneous, since all the segment are already in the mp4 format. Thus, no encoding/decoding needs to be done and the files are just stitched together).
Video preview generation
Once we have the video segments and the playlist files, we can now generated additional files that enhance the viewing experience. After the transcoding and segmentation processes are complete, the program moves onto generate two image files: a poster image file to display before the user clicks on the play button in JW Player, and video preview images to show a thumbnail of the playing video above the seek bar.
- Poster Image
  Generating the poster image is fairly straightforward; the ffmpeg command seeks to a random part of the video and grabs the first frame at that duration and uses it as the poster.
- Preview Images
  Generating the preview images requires extracting the last frame of every 5 second portion of the video. Once the images are extracted, a index file (.vtt file) is created to tell JW Player which image to display at which portion of the video. Ffmpeg doesn't generate this file automatically and hence it must be generated by our program manually.
  One issue faced during this process was that the process was producing too many image files and it could cause problems when going large scale. Hence, instead of producing a large number of images, one image was produced with the different preview images stitched together to produce one image strip. The index file has to be already to reflect this; .vtt files support image strips by allowing users to define the x and y coordinates of the top-left corner of the image.
## Data
Upon testing, it was discovered that probing takes a fixed amount of time regardless of the input file bit rate or duration – 0.5s for probing the audio stream and 0.5s for probing the video stream.
The relationship between input file duration and bit rate, and the time taken to perform various parts of the video processing can be seen below:
To further illustrate the effect of changing bit rate and file duration, further testing was performed. The table below shows the effect of increasing file duration on the time taken to process a video. We can observe that the time taken to transcode and segment a file requires the same proportion of the input file duration (i.e. time is increasing at a constant rate) , whereas the time for poster generation is increasing at a decreasing rate (seen by the gradual decrease in the value of P+P Time/Input Time).
The table below shows the effect of increasing bit rate on the time taken to process a video. We can observe that the time taken to transcode and segment a file is heavily influenced by the bit rate, seen by the increasing proportion of the input file duration, whereas the time for poster generation is near-about the same, indicating that it is not heavily influenced by a changing bit-rate.

Summary:
- Probing – Unaffected by file duration or file bit rate (Constant at 0.5s for each stream)
- Transcoding+Segmentation – Increases with both file duration and file bit rate
- Preview+Poster – Increases with file duration

## Parallel, Scalable Transcoding
The system described above works perfectly well for transcoding one file manually. But to incorporate this system into a large project, it needs to work faster and handle much, much more than single file. A potential system that can be used in large-scale operations is outlined below.
- Queuing Mechanism
  All incoming files will be queued in a queuing mechanism. The Master Node will pick the first file at the head of the queue to transcode and segment.
- Master Node
  The node that acts as a controller between the queue and the worker nodes. The master node will take the file at the head of the queue and store the it into the shared file space. It will then perform the probe part of the transcoding process described above and store the meta-data into a database that can be accessed by all the worker nodes. Once the probing is complete, the master node will delegate the transcoding and segmenting onto the worker nodes. While the worker nodes are processing their respective chunks of the file, the master node will perform the video preview generation, and store the generated files into the shared file space. Once all the nodes raise their respective flag, the master node will perform the combining process and produce the play lists and master.m3u8.
- Worker Nodes
  Nodes to perform the transcoding and segmentation. These nodes will work on their chunks of the input file and store the output in the shared file space. Once the node has completed its work, it will raise a flag to signal to the master node that it has completed its task. Since all the nodes will create separate play lists for their chunks of the file, they need to be combined to produce one play list for each resolution (done by the master node). All the generated files are stored in the shared file space.
- Shared File Space
  A shared file space where all the input and output files can be stored.
Sample run
A sample run to illustrate the concept of parallel transcoding was done; the results are below:
Parallel Transcoding
No. of Nodes
Time Taken (ms)
The same program described in the earlier sections was altered to support a distrusted and scalable video processing solution.